PROGRAMMING WITH THE HP-IL PRIMITIVES INTERRUPT (INT 54h)




                            Copyright July 1987   
                          Hewlett-Packard Company





        Although the HP 82973A Portable-Desktop Link is designed to be
        a file transfer utility, you can use the card for controlling
        HP-IL devices.  HP-IL can also be used to control HP-IB (IEEE-488) 
        devices through an HP82169 HP-IL/HP-IB interface.  Each device 
        driver communicates with its device by calling HP-IL primitive 
        routines.


        WHO IS THIS DOCUMENT FOR?
        
        This information is provided for programmers who wish
        to control HP-IL from within their applications using low-level
        MS-DOS primitives.  These primitives are provided to the 
        programmer using Interrupt 54h.  With the HP-IL driver installed
        in your desktop PC, you have Interrupt 54h available to you. 
        This interrupt enables your PC to be a system controller on HP-IL.
        (Your PC can't be a device on HP-IL with this driver.)

      

        THE HP-IL DRIVER

        The files HPIL.SYS, HPIL_PRN.SYS, and HPIL_LPT.SYS are drivers.
        Before you run a program that uses interrupt 54, you must have
        one of these drivers installed in DOS.  To install a driver in
        DOS, you must include a line similar to the following in the
        file called CONFIG.SYS:
        
                DEVICE = HPIL.SYS

        When you reboot your PC, the HP-IL driver will be installed, making
        interrupt 54 available to your program.  (For more information,
        refer to the owner's and programming documentation for your PC.)
        
        Instruments and other devices not currently supported by MS-DOS
        device drivers may also be controlled with a suitable application
        program.  The application programmmer can call these same HP-IL
        primitives to communicate with the device to be controlled.  Using
        these routines will simplify the program and allow the application
        to share the bus with the MS-DOS drivers without conflict.  It is
        recommended that devices which have MS-DOS drivers be controlled
        through standard MS-DOS system calls and that HP-IL primitives be
        used only for unsupported devices.

        HP-IL Primitives Interrupt 54h is used to invoke the various
        primitive functions, which in turn provide low level control of the
        HP-IL interface and serve to isolate from each other the various
        routines that use HP-IL.  For example, an application can read data
        from an HP-IL voltmeter, use MS-DOS Int 21h functions to print the
        data, and save the data on an HP-IL disc without any conflicts.

        By using Int 54h, the application programmer can do the following
        operations:

        * Configure the loop and assign addresses to all the devices on it.

        * Address any device to either send data or receive it.

        * Send data bytes to any device on the loop.

        * Receive data bytes from any device on the loop.

        * Send or receive individual frames.

        * Search for devices according to their accessory IDs.

        * Set the expected time out period for each operation.

        * Read interface status information.

        * Read the Accessory ID of any device on the loop.

        * Search the loop for a device with a certain accessory ID.


        CONTROLLING HP-IL DEVICES

        Many instruments can be controlled by simply sending data bytes and
        receiving information back.  For example, to instruct an HP 3421A
        Data Acquisition unit to take a voltage reading and report the
        results requires the following steps:

          1. Configure the loop to put it into a known state.

          2. Locate the HP 3421A and determine its address.

          3. Address the Portable PLUS to talk and the HP 3421A to listen.

          4. Set the time out to an approriate value for the HP 3421A.

          5. Send the data bytes "DCV<cr>".

          6. Address the HP 3421A to talk and the Portable PLUS to listen.

          7. Receive the data bytes that the HP-3421A returns.

        Other instruments may require the application to directly send HP-IL
        loop commands and be able to respond to service requests.  An
        application can directly send and receive HP-IL frames and so can
        generate any command sequence that an instrument may require.  A
        thorough description of HP-IL can be found in the
        Osborne/McGraw-Hill publication: 

                The HP-IL System: An Introductory Guide to the 
                Hewlett-Packard Interface Loop, by Kane, Harper, and
                Ushijima (1982).


        THE HP-IL PRIMITIVES

        The HP-IL primitives provide the low level control over the HP-IL
        interface in the Vectra.  They permit an application to
        interleave I/O operations and allow optimizations that lead to more
        efficient operation.  The routines keep track of loop information
        such as the time of the last frame transmission and the current
        state of the loop.  If a command is given that would be unnecessary
        due to the current state of the loop then it will be safely ignored.
        For example if an application issues an Address command for devices
        that are currently addressed then no frames will be sent.

        Before each major group of operations (or any time the caller cannot
        be sure of the loop configuration) the Config function must be
        called.  No frames will be sent during this call if it has been only
        a short time since the most recent loop operation.  Note that
        because this call checks the time since the previous loop operation,
        any HP-IL operations performed immediately before the call will
        cause the Config call to be ignored.


        Each HP-IL function returns a completion code in AL and error status
        in the CY (Carry) flag.  The remaining flags and registers are not
        changed.  If the function fails due to a loop problem (ie. not
        connected or one or more devices turned off) then it will set the
        carry flag and return an error code.  The following bits will be set
        for errors:

          +----------------------------+
          | 0  0  0  0  0  b2  b1  b0  |   HP-IL Error Code Byte
          +----------------------------+
                            |   |   |
                            |   |   +--- = Device/Loop not ready
                            |   +------- = Timeout
                            +----------- = Frame received not as sent

        In most cases an error requires that the application use the Config
        command to restore the loop to a known state.  Applications that
        issue Send Frame and Get Frame commands may have to process the
        error according to which command was sent over the loop.  For
        example if the application sends an autoaddress command frame it
        will be modified by any devices in the loop and cause the HP-IL
        interface to issue a "Frame Received Not as Sent" error.  In this
        case, the error is expected and can be ignored by the application.
        However, if a Config command fails, user intervention may be needed
        to restore the loop.

        If a Timeout is indicated, the next call will generate a power up
        sequence (multiple IFCs followed by a single RFC).  This sequence is
        also performed before the first function call after power on.  This
        standard timeout recovery may not be overridden.

        After configuring the loop the application must determine the
        address of the device that it is controlling.  If it is a HP-IB
        device that is connected via a HP 82169A interface then the address
        will be the same as the HP-IB address.  If the device is an HP-IL
        device then it will be autoaddressed according to its position on
        the loop.  Note that the user should be careful when choosing HP-IB
        device addresses since it is possible to have an HP-IB and an HP-IL
        device that both respond to the same address.  Only addresses 0
        through 7 are allowed for HP-IB devices.  HP-IL addresses will then
        start at 8 and be sequentially assigned to all devices around the
        loop.

        For HP-IL devices the best way for an application to determine the
        address of a device is with Accessory IDs.  If the device supports
        this feature then the application can issue a Find command that will
        return the address of the desired device.  An application that uses
        the Find function will not be dependent on the order that the
        devices are placed on the loop.  An alternative way to locate
        devices is to request a device to talk and use the Input Data Block
        command to enter a device ID.  This is normally an ASCII string that
        identifies the particular device.

        Most of these routines require the Portable PLUS to be the active
        controller on the loop, although some applications (such as HPLINK)
        use the computer as a non-controller.  Any application that passes
        control of the loop to another device must regain control before
        making any MS-DOS calls that could require use of the loop.


        A typical character device driver will call the HP-IL functions in
        the following order for each character to be sent to the target
        device:

           Config         ;Configure the loop if necessary
           Find           ;Find desired device
           Address        ;Address device to listen

           ;No frames are sent above under normal conditions

           SetTimeout     ;Set to reasonable value for device
           SendFrame      ;Send byte ("Output" also valid here)
           .
           .
           .

        A typical block device driver will perform HP-IL operations in the
        following order:

           Config         ;Check loop configuration
           Find           ;Find disk drive
           SetTimeout
           SendFrame      ;Use "SendFrame" for specific frame sequence
           .
           .
           .

        Table 1 (beginning on the next page) describes the HP-IL primitives 
        interrupt functions.


        Table 1.  HP-IL Primitives Interrupt 54h Functions
        --------------------------------------------------------------------
         Function                 Description
        --------------------------------------------------------------------
         AH=0      Configure Loop
         (00h)
                The Configure Loop primitive checks the elapsed time
                since the last HP-IL operation and performs loop
                configuration if necessary.  This function should be
                called before each major group of loop operations to
                ensure correct configuration.  No frames are sent unless
                absolutely necessary.  Configuring the loop consists of
                giving each device an address according to its position
                on the loop.  The first device on the loop is given
                address 8, the second device is address 9, and so on up
                through a maximum of 23 devices.  (Addresses 0-7 are
                reserved for HP-IB devices that may be connected to the
                loop through a HP 82169A HP-IL/HP-IB Interface.)  If 23
                or more devices exist on the loop, all devices beyond
                the first 22 are assigned address 30 (decimal).

                Returns:
                 AL = Completion code.


         AH=1      Find Device
         (01h)
                This primitive searches the loop starting at the address
                specified in BH, looking for a device with an accessory
                ID that matches the one in BL.  If the value of BL is
                xFh, only a class match is performed (only the top four
                bits are compared with the device accessory IDs).  If a
                matching device is found, its address is returned in BL.
                The BIOS maintains a table of all devices that have been
                found on the loop and will return data from this table
                if it is available.  No frames are sent unless
                absolutely necessary.

                Specify:
                 BH = Starting address (00h-1Eh).
                 BL = Desired accessory ID (00h-FFh, excluding FEh).

                Returns:
                 AL = Completion code.
                 BL = Address of device (1Fh if not found).

                Destroys:
                 BH



        --------------------------------------------------------------------
        Table 1.  HP-IL Primitives Interrupt 54h Functions (Continued)
        --------------------------------------------------------------------
         AH=2      Get Accessory ID
         (02h)
                This primitive returns the accessory ID of the HP-IL
                device at the address specified in BL.  Several
                conditions exist that will cause a value of FEh to be
                returned:

                1) Addressed device does not support accessory ID.
                2) Addressed device does not exist.
                3) Addressed device has an accessory ID of FEh.  FEh is
                   the ID for an Extended class, General device.  A program 
                   that needs to control a device with this ID will require
                   some other means to determine if the device is on the loop.

                No frames will be sent unless absolutely necessary.

                Specify:
                 BL = Device address.

                Returns:
                 AL = Completion code.
                 BL = Accessory ID. (FEh = no device at address, device
                      doesn't support accessory ID, or accessory ID
                      is FEh.)

                Destroys:
                 BH




        --------------------------------------------------------------------
        Table 1.  HP-IL Primitives Interrupt 54h Functions (Continued)
        --------------------------------------------------------------------
         AH=3      Address
         (03h)
                This function prepares the loop for a data transfer
                between the computer and a device on the loop.  It is
                used before an Input Data Block or Output Data Block
                primitive to select the device that will either supply
                or receive data.  The address of the selected device is
                sent as either a talk or listen address while 1Fh
                designates the address for the Portable PLUS itself.
                The BIOS keeps track of which devices are currently
                addressed as talker and listener and will only send an
                address command if they are changed.  Setting both talk
                address and listen address to 1Fh is a special case that
                sends UNTalk and UNListen commands to all other devices
                on the loop.

                These HP-IL primitives do not support direct data
                transfer between two other devices on the loop.  All
                transfers must go through the Portable PLUS.  If direct
                transfer is required then the application programmer
                must use the Send Frame primitive to address the loop
                and start the transmission of data.

                Specify:
                 BH = Talker address (00h-1Eh or 1Fh).
                 BL = Listener address (00h-1Eh or 1Fh).

                Returns:
                 AL = Completion code.
                 BH = Old talker address.
                 BL = Old listener address.

                Destroys:
                 DX 


        --------------------------------------------------------------------
        Table 1.  HP-IL Primitives Interrupt 54h Functions (Continued)
        --------------------------------------------------------------------
         AH=4      Output Data Block
         (04h)
                The Output Data Block primitive causes the block of CX
                bytes of data at location ES:DI to be sent over the
                loop.  If the End Option is set to 1, the last byte of
                data is sent as an END frame.  If DI+CX is greater than
                65536, a segment wraparound will occur and incorrect
                data may be sent.

                Specify:
                 CX    = Byte count (0 - 65,536).
                 DX    = End option (0 - 1).
                 ES:DI = Address of buffer containing data to be sent.

                Returns:
                 AL = Completion code.
                 CX = Number of bytes actually transfered.

         AH=5      Input Data Block
         (05h)
                This primitive reads CX bytes of data from the loop into
                a buffer at location ES:DI.  If BX is a valid SOT frame,
                it is sent out to initiate the transfer.  If BX is 00h
                or not an SOT frame, the transfer is assumed to have
                already been started.  (Valid SOT frames include SDA,
                SST, SDI and SAI(1)).  The transfer will terminate when
                all CX bytes have been received or when an ETO is
                received.  If the buffer fills before ETO is received,
                an NRD sequence is transmitted.  There is an ambiguity
                that occurs when the caller tries to input exactly 65536
                bytes; this routine will return CX=0 for both the case
                of a successful operation and the case where no bytes
                are received.

                   SDA 560h   Send Data
                   SST 561h   Send Status
                   SDI 562h   Send Device ID
                   SAI 563h   Send Accessory ID

                Specify:
                 BX    = Optional SOT frame to be sent ("0" = none).
                 CX    = Count of bytes to accept before NRD.
                 ES:DI = Pointer to data buffer.

                Returns:
                 AL = Completion code.
                 CX = Count of bytes received.


        --------------------------------------------------------------------
        Table 1.  HP-IL Primitives Interrupt 54h Functions (Continued)
        --------------------------------------------------------------------
         AH=6      Send Frame
         (06h)
                The specified frame is sent out over the loop and an
                error code is returned.  Frame is the frame value
                (0-2047) to be sent.  The values and their usage are
                defined in the HP-IL interface specification manual,
                which should be consulted if the programmer needs this
                level of interface control.  The options supported are
                "Wait For Loop Ready Before Transmit" (DX=0) and "No
                Wait Before Transmit" (DX=1).
                Specify:
                 BX = Frame to be sent (00h-7FFh).
                 DX = Wait option (0=wait; 1=no wait).
                Returns:
                 AL = Completion code.

         AH=7      Get Frame
         (07h)
                This primitive waits for a frame to be received, and
                returns it in BX.  If no frame is available from the
                HP-IL interface then 00h is returned.  Get Frame is
                normally used in conjunction with the Send Frame
                primitive when the programmer must have complete control
                of the Loop.
                Returns:
                 AL = Completion code.
                 BX = Received frame (DAB0h=Frame unavailable).


        --------------------------------------------------------------------
        Table 1.  HP-IL Primitives Interrupt 54h Functions (Continued)
        --------------------------------------------------------------------
         AH=8      Status
         (08h)
                Returns current loop status in BX.  If the loop is ready
                for a frame to be sent, bit 0 will be set.  If a frame
                is available, then bit 1 will be set.  Note that any
                operation that sends a frame will effectively erase the
                frame available bit.  The timeout is also tested if the
                loop is not ready for a frame, and a timeout error is
                returned if necessary.
                Returns:
                 AL = Completion code.
                 BX = Status:
                     Bit 15-7: (Not used.)
                     Bit 6: Controller active.
                     Bit 5: Talker active.
                     Bit 4: Listener active.
                     Bit 3: Service request received.
                     Bit 2: (Not used.)
                     Bit 1: Frame available.
                     Bit 0: Loop ready for frame.


         AH=10     Set Timeout
         (0Ah)
                An HP-IL device that sends data can perform a loop test
                on each byte sent by comparing the byte it sends with
                the byte that returns after traveling around the loop.
                By specifying a timeout interval, an application can
                dictate how long the HP-IL driver should wait for a
                response to each byte sent out over the loop.  If a
                device response is not detected by the time the timeout
                period has elapsed, an error is declared and control is
                returned to the calling application.

                Variable timeout periods allow the programmer to handle
                devices that require a long period of time to complete
                their operation.  For example a printer may take 20
                seconds to do a formfeed and hold up the loop during
                that period of time.
                Specify:
                 BX = New timeout (in 1/16 seconds).
                Returns:
                 AL = Completion code.
                 BX = Old timeout (in 1/16 seconds).

     -----------------------------------------------------------------------


        EXAMPLE

        This program demonstrates using the BIOS HP-IL interrupt
        (54h) to talk to a device on HP-IL.  In this case, the device is an
        HP 3421A Data Acquisition/Control Unit.  The program:

          1. Configures the loop and sets the loop timeout value.

          2. Finds the HP 3421's loop address.

          3. Addresses the HP 3421 to listen and sends the "Read Voltage"
             command to it.

          4. Addresses the HP 3421 to talk and enters the voltage reading.

          5. Displays the voltage read.

          6. Exits.

        The program is structured to be run through EXE2BIN (converted to a
        .COM program) and therefore doesn't set up DS, ES, or SS, since
        MS-DOS does that before passing control to the program.

     page 60,132
     title INSTRUMENT CONTROL --- using the BIOS HP-IL interrupt
     ;
     cseg segment para public 'code'
          assume  cs:cseg, ds:cseg
          org  100h
     start     proc far
          call config              ; configure the loop
          call find                ; find the HP 3421
          call output              ; send the READ VOLTAGE command
          call enter               ; enter the voltage
          mov  dx,offset buffer    ; address of string
          mov  ah,9                ; display it
          int  21h
          mov  ax,4c00h            ; terminate our program
          int  21h
     start     endp
          page


     ;
     ; CONFIG --- configures the loop into known state & assigns 
     ;            addresses terminates with ERRORLEVEL=1 if timeout
     ;
     config:
          mov  ah,0                ; configure the loop
          int  54h                 ; BIOS HP-IL call
          test al,7                ; not ready?
          jnz  error1              ; jif yes
          mov  ah,10               ; set timeout
          mov  bx,64               ;   for 4 seconds (64*(1/16))=4
          int  54h
          test al,7                ; not ready?
          jnz  error1              ; jif yes
          ret                      ; else keep going
     error1:
          mov  dx,offset loopfail  ; address of error message
          mov  al,1                ; errorlevel=1
     error:
          push ax                  ; save errorlevel
          mov  ah,9                ; DOS funct to display message
          int  21h
          pop  ax                  ; recover errorlevel code
          mov  ah,4ch              ; terminate code
          int  21h                 ; terminate
          page
     ;
     ; FIND --- finds a device on the loop by its accessory ID
     ;         terminates with ERRORLEVEL=2 if not found
     ;
     find:
          mov  ah,1                ; find function
          mov  bh,0                ; starting search address
          mov  bl,53h              ; accessory ID for HP 3421
          int  54h                 ; BIOS HP-IL call
          test al,7                ; not ready?
          jnz  error2              ; jif yes
          cmp  bl,1fh              ; not found?
          jz   error2              ; jif yes
          mov  address,bl          ; else save the address
          ret
     error2:
          mov  dx,offset nodevice  ; address of error message
          mov  al,2                ; errorlevel
          jmp  error
          page


     ;
     ; OUTPUT --- sends the READ VOLTAGE command to the HP 3421.
     ;         terminates with ERRORLEVEL=3 if fails.
     ;
     output:
          mov  ah,3                ; address the loop
          mov  bl,address          ; get HP 3421 address (LISTENER)
          mov  bh,1fh              ; get PC address (Talker)
          int  54h                 ; BIOS HP-IL call
          test al,7                ; any problems?
          jnz  error3              ; jif yes
          mov  ah,4                ; send data block
          mov  dx,1                ; finish with END frame
          mov  cx,5                ; length of command
          mov  di,offset command   ; address of the command
          int  54h
          test al,7                ; any problems?
          jnz  error3              ; jif yes
          cmp  cx,5                ; all bytes transferred?
          jnz  error3              ; jif no
          ret
     error3:
          mov  dx,offset sendfail  ; address of error message
          mov  al,3                ; set errorlevel
          jmp  error
          page
     ;
     ; ENTER --- read the voltage back from the HP 3421
     ;         terminate with errorlevel=4 if fails.
     ;
     enter:
          mov  ah,3                ; do loop addressing
          mov  bh,address          ; address of TALKER (HP 3421)
          mov  bl,1fh              ; addr of LISTENER (PC)
          int  54h                 ; BIOS HP-IL call
          test al,7                ; any problems?
          jnz  error4              ; jif yes
          mov  cx,32               ; max number of bytes to read
          mov  bx,560h             ; SDA (Send DAta) command
          mov  di,offset buffer    ; address of scratch buffer
          mov  ah,5                ; input data block
          int  54h
          test al,7                ; any problems?
          jnz  error4              ; jif yes
          mov  di,offset buffer    ; address of start of data
          add  di,cx               ; move to end of data
          mov  ax,0a0dh            ; CR/LF
          stosw
          mov  al,36               ; ascii for $
          stosb                    ; terminate string
          ret
     error4:
          mov  dx,offset entrfail  ; address of error message
          mov  al,4                ; errorlevel
          jmp  error
          page


     ;
     ;
     loopfail  db   'Loop failure',13,10,'$'
     nodevice  db   'Device not found',13,10,'$'
     sendfail  db   'Send failure',13,10,'$'
     entrfail  db   'Enter failure',13,10,'$'
     command   db   'DCV',13,10
     ;
     ;
     address db     ?                   ; address of HP 3421
     buffer  db     32 dup (?)          ; scratch buffer
     ;
     cseg ends
          end  start